| EECS 322 | Sample Test 1 | Wednesday February 14, 2001 |
| --- | --- | --- |

| Name: |  |  |
| --- | --- | --- |

Problem 1 (18%). Assemble the following machine instructions into binary, use spaces to separate fields, and registers in their symbolic form ($ra NOT $31). Assume absolute jump addresses.

| Field 1 | Fields 2 and etc | instruction |
| --- | --- | --- |
| 100011 | 00011 11111 0000000000001100 | lw $ra, 12($v1) |
| 001000 | 10010 11001 0000000011111010 | addi $t9, $s2, 0xFA |
| 000000 | 00000 11101 00100 11100 000000 | sll $a0,$sp,0x1C |
| 000000 | 01011 00000 00101 00000 100000 | move $a1,$t3 |
| 000011 | 00000000000000000000010100 | jal $20 |
| 000000 | 1 0 0 1 0 0 1 0 0 0 0 1 0 0 0 0 0 0 0 0 1 0 0 0 0 | add $t0,$s2,$t0 |

Problem 2 (7%).

Assume each part is independent. Assume absolute jump & branch addresses (no pc relative).

Fill in only registers that changed!

What is the value of the register or memory contents after the execution of the instruction.

Assume  pc = 1000;   $t1=12;  $t2=3;  $ra=50;  memory[12]=0x17761453;

| instruction | pc | $ra | $t1 | memory[12] |
| --- | --- | --- | --- | --- |
| lw $ra, 12($0) | 1004 | 0x17761453 |  |  |
| addi $t1, $t2, 0x01 | 1004 |  | 4 |  |
| sll $t1,$t2,2 | 1004 |  | 12 |  |
| clear $t1 | 1004 |  | 0 |  |
| jal $20 | 20 | 1004 |  |  |
| bge $t1,$t2,40 | 40 |  |  |  |
| ble $t1,$t2,40 | 1008 |  |  |  |

Problem 3. (25%) Translate the following C code into MIPS. Please comment your code.

Assume x is $s0; y is $s1; p is $a0 and points to integers; s is $a1 and points to unsigned char.

Points will be taken off for assembler syntax errors.

- x  = (x + (y – 3)) & 0xFF;

addi		$t0, $s1, –3

add		$t0, $s0, $t1

andi		$s0, $t0, 0xFF

- x  =  (y > 3)? x + 1 : x – 1;

addi		$t0, $zero, 3

slt		$t1, $t0, $s1		# if ((3 < y )== 0) goto L1

beq		$t1, $zero, L1

addi		$s0, $s0, 1		# then

j		L2

L1:	addi		$s0, $s0, –1		# else

L2:

- for(x=1;   x;   x++ )   {  y++;  }

addi		$s0, $zero, 1		# x = 1;

L2:	beq		$s0, $zero, L1		# if (x = = 0) goto L1

addi		$s1, $s1, 1		# y++ sames y=y+1

addi		$s0, $s0, 1		# x++

j		L2;

L1:

(d)  p[5]   =   *p +  y + *s;   /*note: same as  *(p+5)  =  *(p+0)  + y  + *(s + 0) */

lbu		$t0,0($a1)	# *s   (points to unsigned char)

add		$t1,$t0,$s1	# + y

lw		$t2,0($a0)	# *p   (points to int)

add		$t3, $t2, $t1	# *p + y + *s

addi		$t4,$zero,20	# 5 * sizeof(int) = 5*4 = 20

add		$t5,$t4,$a0	# address of p[5]

sw		$t3,0($t5)	# *(p+5) =

(e)  p[x+3]  = s[x+2]  |  0x01   /* note: same as *(p+x+3) = *(s+x+2 ) | 0x01 */

addi		$t0,$s0,2			# x + 2

add		$t1,$a1,$t0		# (s + x + 2)

lbu		$t2,0($t1)		# = *(s + x + 2)

ori		$t3,$t2,0x01

addi		$t4,$s0,3			# x+3

add		$t5,$t4,$t4		# 2*(x+2)

add		$t6,$t5,$t5		# 4*(x+2)

add		$t7,$a0,$t6		# p + x + 2

sw		$t3,0($t7)		# *(p+x+2) = $t3

Problem 4. (25%)  Translate the following code and add comments

void	rgcd(int x, int y)  {

register int  w=0, z=1;

if (y = = 0)  { return x; }

z = x + y;

w = rgcd(y, z);

return w + z;

}

- Write the prolog

.text			# read appendix A.6 and A

rgcd:

add	$sp,$sp –12		# allocate space

sw	$ra,8($sp)

sw	$s1,4($sp)

addi	$s1,$zero,1		# z = 1;

sw	$s0,0($sp)

add	$s0,$zero,$zero	# w = 0

- Write the body

bne	$a1,$zero,rgcd2		# if (y != 0) goto rgcd2

add	$v0,$a0,$zero		# return x

j	rgcd_epilog

rgcd2:

add	$s1,$a0,$a1			# z=x + y

add	$a0,$a1,$zero		# $a0 = y

add	$a1,$s1,$zero		# $a1 = z

jal	rgcd

add	$s0,$v0,$zero		# w = return

add	$v0,$s0,$s1			# return = w+z

(c) Write the epilog

rgcd_epilog:					# not require to retore $a0, $a1

lw	$s0,0($sp)		# restore caller’s $s0

lw	$s1,4($sp)		# restore caller’s $s1

lw	$ra,8(sp$)

addi	$sp,$sp,12		#free space

jr	$ra

Problem 5. (10%)  Translate the following global variables

- char x[6] = “hello”;

.data

x:		.byte	‘h’,’e’,’l’,’l’,’o’,0

- struct treenode {

struct treenode *left, *right;

char	symbol[4];

} root;

.data

root:

root_left:		.word	0

root_right:		.word	0

root_symbol:		.byte	0,0,0,0

Problem 6. (15%)  Given the following instruction sequence in the table below.

Assume the (alu instructions are 6 clocks); (loads 8 clocks); (stores 7 clocks); (jumps 2 clocks); (branches 5 fall through/8 for branch);

(a)  Show the best case timing path through the code showing annotations and total.

(b)  Show the worst case timing path through the code showing annotations and total.

(c)  What values will make this code execute the worst case?

$s0 = 0  and $s1 = 3

| instruction | best case | worst case |
| --- | --- | --- |
| bne $s0,$zero,L2 | 8 branch | 5 fall through 5 fall |
| addi $t0,$zero,3 |  | 6 alu 6 alu |
| bne $s1,$t0,L2 |  | 5 fall through 8 branch |
| addi $s1,$s1,1 |  | 6 alu |
| j L1 |  | 2 jump |
| L2: addi $s1,$zero,10 | 6 alu | 6 alu |
| L1: |  |  |
| Time | 14 clocks | 24 clocks 25 clocks¹ (correct) |

¹correct answer due to a quick thinking student

# Text boxes

# alternate solution

addi		$t0,$s0,2

add		$t1,$a1,$t0

lbu		$t2,0($t1)

ori		$t3,$t2,0x01

addi		$t4,$s0,3

add		$t5,$s0,$s0

add		$t6,$t5,$t5

add		$t7,$a0,$t6

sw		$t3,12($t7)

see problem 3.10 pseudoinstructions.

slt     $at,$t2,$t1

beq   $at, $zero,  40